## Slide 1: STUDY ON FIBER OPTIC CURRENT TRANSFORMERS

## Slide 2: INTRODUCTION
With the rapid development of power system and the increase of voltage level of transmission and distribution, the traditional electromagnetic current transformer exposed a series of faults such as
    Complex insulating construction
    High manufacturing cost
    Combustile & explosive character
    Nonlinear factors of ferrous core such as eddy current , hysteresis loss and phase error caused by windings

## Slide 3: DIFFERENCE BETWEEN CT & FOCT
Oil filled conventional CTs works on the principle of electromagnetic induction

## Slide 4: PRINCIPLE OF OPERATION OF FOCT

## Slide 5
Faraday discovered that when a block of glass is subjected to a strong magnetic field, it becomes optically active. When plane-polarized light is sent through the glass in a direction parallel to the applied magnetic field, the plane of vibration is rotated.
This rotation can be expressed by the relation

## Slide 7: DIFFERENT FOCT
ROGOWSKI COIL FOCT
FARADAY ROTATION FOCT
SPUNFIBER FOCT
MAGNETO-OPTIC BALANCE TYPE OF FOCT

## Slide 8: 1ROGOWSKI COIL FOCT
Principle of operation

## Slide 9: Signal processing
On the HV side
    E/O CONVERSION
    A/D CONVERSION
    V/F CONVERSION
On the LV side
    O/E CONVERSION
    TIMER
    FREQUENCY COUNTER
    Received frequency=D/T
    (D=count value of frequency counter T=Count time of counter)
    Optical fiber supply is used to drive various electronic devices in HV side.

## Slide 10: 2 FARADAY ROTATION FOCT 2

## Slide 11
Light from source is linearly by polarizer after passing through coupler.
The tails of fiber polarizer and modulator are welded with 45°, therefore the linearly polarized light is split into orthogonal polarization.
Next, the two orthogonal linear polarizations is converted into left and right circular polarizations at fiber λ/4 retarder and enter the sensing fiber looped around an electric current.
The circular polarizations are propagating in the sensing fiber with different speed and direction, and reflected on a mirror at the end the sensing fiber, and then come back to the fiber coil in the reverse direction.
In the propagation, the current-generated magnetic field produces a nonreciprocal phase shift between two lights by Faraday effect
The Faraday rotation angle θ is given by θ=4VNI
After passing through the modulator, the two lights interfere and are detected by optical receiver where lights are converted to electrical signals. Finally, by a signal processing circuit, output signal proportional to the current is produced.

## Slide 13: Problems faced with FARADAY FOCT
FARADAY FOCT suffers the linear birefringence effect which originates from the optical fiber’s axial asymmetry and the environmental perturbations such as temperature drift, vibration, resonating frequency etc.

## Slide 14: COMPENSATION METHODS FOR LINEAR BIREFRINGENCE
1) Low birefringence fiber which has minimum Birefringence
2) Twisted fiber which was twisted to generate
enough circular birefringence to quench the linear one
3)Annealed fiber which suppress the stress-induced birefringence by heating the sensor coil.
5) Flint glass fiber which contains lead
6) Spun fiber

## Slide 15: 3 FOCT WITH SPUN FIBER SENSOR COIL
Spun fiber is produced by spinning the fiber preform during the drawing process.
The circular birefringence induced in the spun fiber cancels out and prevent the linear birefringence from accumulating.
Compared with twisted fiber, spun fiber does not have internal stress caused by twisting and is much easier to handle.

## Slide 17: 4 MAGNETO-OPTIC BALANCE TYPE OF FOCT

## Slide 18
The major merit of this topology is that the linear relationship between measured quantity and detectable quantity still exists without loss of accuracy even if the linear birefringence in optic fiber CTs is high.

## Slide 20: ADVANTAGE OF FOCT
Absence of saturation of core
Excellent electrical isolation
Small size ,light weight and low production cost
Can measure DC
Antielectromagnetic interference characteristics
Does not need power supply in HV side
High speed of response
Transmit digital signal so easy to interface with a communication network
The sensor element is naturally decoupled from the voltage line.

## Slide 21: CONCLUSION
Number of technical shortcomings such as unacceptable sensitivity to temperature and vibration as well as concerns about their long term reliability have contributed to prevent their widespread practical application.
With the development of technique, these problems have gradually been solved and more and more smart substations have equipped with the FOCTs.

## Slide 22: REFERENCES
Wang Na &Wan Quan. “Application of the Fiber Optical Current Transformerin the 110kV Smart Substation” 978-1-4577-0547-2/12/$31.00 ©2012 IEEE
Wang Yutian Yuan Jing ∗ Wang Huixin Liu Jie.“Design and research of fiber optically powered Rogowski coil current transformer”, Procedia Engineering 15 (2011) 886 – 890
Tang Ming-jie , Cao Jian-an.” Study on Magneto-Optic Balance Type of Optical Fiber Current Transformer Used in Extra-High Voltage Measurement”. 2011 Third International Conference on Measuring Technology and Mechatronics Automation
Hyoung-Jun Park, Hyun-Jin Kim and Minho Song. “A fiber-optic current transformer with spun fiber sensor coil” The International Conference on Electrical Engineering 2008
WeiBing Hu, KaiCheng Li , and JianFeng Liu“RESEARCH ON DIGITAL OPTICS FIBER CURRENT TRANSFORMER.” UPEC 2007 – 509

## Slide 23: THANK YOU